## Slide 1
PROJECT PROGRESS REVIEW 1
Physics-Informed Deep Neural Network for Digital Twin Modeling of UAV-to-Ground Wireless Channels
Wireless Communications · Deep Learning · Digital Twins
Team Members
[S.HARSHITHA] — [2520040017]
[P.SRINIDHI] — [2520040016]
Guide: [NL PRASAD]
Department: [ECE], KL University, Hyderabad
Academic Year 2025–26

## Slide 2
Agenda
Problem Statement
Objectives
Literature Survey
System Architecture
Dataset & Input / Output Parameters
Physics Model (FSPL)
PI-DNN Model & Loss Function
Baseline vs. Physics-Informed Model
Evaluation Metrics
Digital Twin
KL University, Hyderabad | Progress Review 1
2

## Slide 3
Problem Statement
UAV-to-ground wireless channels are highly dynamic because of changes in altitude, distance, UAV movement, obstacles, and multipath propagation.
Why this problem matters:
Existing approaches either require extensive real-world measurements, or rely only on data-driven models that may not generalize well to unseen conditions.
The need: a physically consistent and efficient model capable of predicting UAV-to-ground channel characteristics for different scenarios.
Our goal: predict the behavior of a UAV-to-ground wireless channel for different UAV positions and environmental conditions — without requiring physical flight testing for every scenario.
KL University, Hyderabad | Progress Review 1
3
Notes: FACULTY MAY ASK: "What exactly is the problem you are solving?"
YOUR ANSWER: "We are trying to predict the behavior of a UAV-to-ground wireless channel for different UAV positions and environmental conditions — without requiring physical flight testing for every scenario."

## Slide 4
Objectives
Study the characteristics of UAV-to-ground wireless channels.
Collect / generate channel data for different UAV positions and propagation conditions.
Develop a Physics-Informed Deep Neural Network (PI-DNN) combining channel data with wireless propagation principles.
Compare PI-DNN performance with a conventional DNN.
Develop a Digital Twin for virtual simulation of UAV-to-ground communication scenarios.
KL University, Hyderabad | Progress Review 1
4

## Slide 5
Literature Survey
Existing Approach | Method | Advantage | Limitation
Traditional channel models | Mathematical / empirical models | Simple | Limited environmental representation
Machine Learning | ML / DNN | Learns complex patterns | Requires sufficient training data
Deep Learning | DNN | Good nonlinear modeling | May not generalize to unseen scenarios
Physics-Informed DL | Physics + DNN | Uses data + physical knowledge | More complex implementation
Proposed | PI-DNN + Digital Twin | Prediction + virtual simulation | Requires proper physics constraints
KL University, Hyderabad | Progress Review 1
5

## Slide 6
System Architecture
System flow:
UAV Parameters + Channel Measurements → Preprocessing → Physics-Informed DNN → Predicted Channel → Digital Twin
UAV parameters: altitude, distance, position, velocity, and environment.
Preprocessing: data cleaning and normalization of the channel measurements.
Physics-Informed DNN: combines measured data and known wireless propagation physics (Data Loss + Physics Loss).
Digital Twin: virtual UAV, ground station, and channel for simulation and analysis of UAV-to-ground link performance under varied scenarios.
KL University, Hyderabad | Progress Review 1
6

## Slide 7
Dataset & Input / Output Parameters
Inputs
UAV altitude
Horizontal distance
UAV position (x, y, z)
Ground station position
UAV velocity
Environment / obstacle information
Carrier frequency
Transmit power
Outputs (choose one focus)
Path loss
Received signal strength
Channel gain
Received power
Recommended first implementation
Inputs → UAV position + altitude + distance + transmit power
Output → Path loss / received signal strength
KL University, Hyderabad | Progress Review 1
7

## Slide 8
Physics Model (FSPL)
Start with the Free-Space Path Loss (FSPL) model:
PL (dB) = 20 log10(d) + 20 log10(f) + 32.44
d = distance between the UAV and the ground station; f = carrier frequency of transmission.
Larger d or f → higher path loss.
The neural network learns from data, while the physics component ensures that the prediction follows expected wireless propagation behavior.
Later extensions
Path loss · Distance effects · Multipath effects · Line-of-sight / non-line-of-sight conditions
KL University, Hyderabad | Progress Review 1
8

## Slide 9
PI-DNN Model & Loss Function
Network flow:
Input Layer → Dense → ReLU → Dense → ReLU → Dense → Output Layer → Predicted Path Loss
Loss function
Conventional DNN loss uses only data: L = Ldata
PI-DNN adds a physics penalty term: Ltotal = Ldata + λ · Lphysics
Ldata = difference between predicted and measured values
Lphysics = violation of physical propagation behavior
λ = weighting factor
KL University, Hyderabad | Progress Review 1
9
Notes: This loss equation is something faculty may specifically ask about.
L_total = L_data + λ · L_physics, where L_data is the difference between predicted and measured values, L_physics is the violation of physical propagation behavior, and λ is the weighting factor.

## Slide 10
Baseline vs. Physics-Informed Model
Model 1: Conventional DNN
Flow: Input → DNN → Prediction.
Learns purely from measured / simulated data — no explicit physics constraint.
Model 2: Physics-Informed DNN
Flow: Input + Physics Constraints → PI-DNN → Prediction.
Combines data with propagation physics for better generalization to unseen scenarios.
KL University, Hyderabad | Progress Review 1
10

## Slide 11
Evaluation Metrics
Error metrics
MAE = (1/N) Σ |y − ŷ|
MSE = (1/N) Σ (y − ŷ)²
RMSE = √MSE
Also evaluate
Actual vs. predicted path loss
R² score
Prediction error
Generalization to unseen UAV positions
Path-loss prediction accuracy
DNN error vs. PI-DNN error — to be plotted after training runs are complete.
KL University, Hyderabad | Progress Review 1
11

## Slide 12
Digital Twin
Flow:
User Input → PI-DNN → Predicted Output
User input (example)
UAV altitude: 100 m
Horizontal distance: 500 m
Transmit power: 20 dBm
Frequency: 2.4 GHz
Predicted output
Predicted path loss: XX dB
Received power: XX dBm
Channel condition: Good
Future extension: 3D UAV trajectory visualization.
KL University, Hyderabad | Progress Review 1
12

## Slide 13
Thank You
Questions & Feedback welcome